## Slide 1: Solutions to problem 2&3 of HW1
PHYS 8750
Numerical simulation of fluid dynamics

## Slide 2
For the backward scheme, all one needs to do is replace the line 43 of the forward scheme with
  phi(itt) = phi(itt-1)*(1+gamma*delt)
Discussion:
For the backward scheme, λ >0 (Figures b and d), the scheme is only stable when the ∆t is larger than t_thres. For λ <=0, the scheme is always stable (Figures a and c).In terms of convergence, for all values of λ, the ∆t must be very small for the scheme to converge to the real solution.
(b)
(a)
(c)
(d)
Backward scheme

## Slide 3
For the trapezoidal scheme, all one needs to do is replace the line 43 of the forward scheme with
  phi(itt) = phi(itt-1)*(1+0.5*gamma*delt)/(1-0.5*gamma*delt)
Discussion:
For the trapezoidal scheme, the threshold for stability is λ∆t<=0. In this figure, two values of λ (-0.5 and 0.5) are used. Since ∆t is always positive, theoretically, the scheme should be stable for λ<=0, and unstable for λ<=0, which is true (Figures a and b). The scheme converges very well for smaller ∆t (figure a and b, ∆t =0.03,0.003, 0.0003). Then if keep increasing ∆t to larger value (c and d, ∆t =0.25,0.125, 0.05), the error in the amplitude and phase becomes very large, and the scheme no longer converge.
(b)
(a)
(c)
(d)
Trapezoidal scheme

## Slide 4
Conclusions
Comparing the forward, backward and trapezoidal scheme, I find:
The forward and backward schemes are comparable in terms convergence, and the trapezoidal scheme dominates the other two. This is consistent with the fact that the first two are 1 order scheme, while the third is a 2nd order scheme. Thus for the same ∆t, the errors are smaller for the trapezoidal scheme.